## Slide 1: ISC + Open-Channel SSD
BAI Shuhan

## Slide 2
INSIDER
1

## Slide 3: INSIDER
FPGA-based ISC Unit : high reconfigurability / high energy efficiency / support massive parallelism → take both performance and flexibility into account
inside FPGA : hardware-isolation (offloading tasks into different app slot); parallelism (high reconfigurability) (data-level paralparallelism (replicating the processing elements to construct SIMD units) / pipeline-level parallelism (constructing a deep hardware pipeline))
host side : virtual file abstraction → abstract ISC as file operation → no need to develop customized API → reduce the difficultly of programming
drive-side : separate the control / data plane → compute-only abstraction → no need to focus on the details of underlying data movement → reduce the difficultly of programming

## Slide 4: INSIDER
FPGA-based ISC Unit : high reconfigurability / high energy efficiency / support massive parallelism → take both performance and flexibility into account
inside FPGA : hardware-isolation (offloading tasks into different app slot); parallelism (high reconfigurability) (data-level paralparallelism (replicating the processing elements to construct SIMD units) / pipeline-level parallelism (constructing a deep hardware pipeline))
host side : virtual file abstraction → abstract ISC as file operation → no need to develop customized API → reduce the difficultly of programming
drive-side : separate the control / data plane → compute-only abstraction → no need to focus on the details of underlying data movement → reduce the difficultly of programming
OCSSD：give hosts control over
drives' inside

## Slide 5: Adding an easy computation thread to test
Finding the place (in FEMU codes) to intercept data: